## Slide 1: More on Assembly
CSE 2312
Computer Organization and Assembly Language Programming
Vassilis Athitsos
University of Texas at Arlington

## Slide 2: Pseudo-Instructions
A pseudo-instruction is something that:
  When you read assembly code, it looks like a regular instruction.
  When it is translated to binary code, it is translated to multiple actual CPU instructions.
Pseudo-instructions are handy.
  We can write code that is shorter, easier to read, easier to test.
However, if we care about performance:
  We must always be aware of the difference between an actual instruction and a pseudo-instruction.
  We should know how the pseudo-instruction is translated.

## Slide 3: The LDR Pseudo-instruction
ldr rd, [rn]:
ldr rd, [rn, #constant]
  ldr is a regular instruction, that we have been using.
However, ldr can also be used as a pseudo-instruction:
ldr rd, =constant.
  In this usage, constant is a 32-bit number, written in decimal or hexadecimal.
Example: ldr r5, =2014.
  Sets r5 = 2014.

## Slide 4: The LDR Pseudo-instruction
Example: ldr r5, =2014.
  Sets r5 = 2014.
Why do we need this pseudo-instruction?
Why can't we just write: mov r5, #2014
mov r5, constant is a real instruction, that gets translated to a single CPU instruction.
For that to be possible, constant must obey certain rules (must be 8 bits, possibly shifted to the left).

## Slide 5: The LDR Pseudo-instruction
The ldr pseudo-instruction allows us to replace bulky code like:
mov r5, #0x7f
lsl r5, r5, #8
add r5, r5, #0xff
lsl r5, r5, #8
add r5, r5, #0xff
lsl r5, r5, #8
add r5, r5, #0xf0
with a single line:
ldr r5, =7ffffff0

## Slide 6: The PUSH/POP Pseudo-instructions
A typical function preamble looks like this:
sub sp, sp, #20
str lr, [sp, #0]
str r0, [sp, #4]
str r4, [sp, #8]
str r5, [sp, #12]
str r6, [sp, #16]
This can all be replaced with this pseudo-instruction:
push {r0, r4, r5, r6, lr}

## Slide 7: The PUSH/POP Pseudo-instructions
push {r0, r4, r5, r6, lr}
The push pseudo-instruction is translated as follows:
  Decrement the stack pointer as much as is needed to make room for the list of registers that is provided.
  Save the provided list of registers into the stack.

## Slide 8: The PUSH/POP Pseudo-instructions
Similarly, a typical function wrapup looks like this:
ldr lr, [sp, #0]
ldr r0, [sp, #4]
ldr r4, [sp, #8]
ldr r5, [sp, #12]
ldr r6, [sp, #16]
add sp, sp, #20
bx lr
This can all be replaced with this pseudo-instruction:
pop {r0, r4, r5, r6}

## Slide 9: The PUSH/POP Pseudo-instructions
This line will produce a compiler warning:
push {lr, r0, r4, r5, r6}
The warning says:
test1.s:20: Warning: register range not in ascending order
The compiler wants you to order the list of registers in ascending order.
Register lr is really register r14, so should come after the other registers in the list:
push {r0, r4, r5, r6, lr}

## Slide 10: Assembly Directives
A directive is a line that does not specify an instruction, but provides other pieces of information.
For the time being, we will cover these directives:
  equ
  ascii
  asciz
  byte
  word

## Slide 11: The EQU directive
.equ IO_ADDRESS, 0x101f1000
... (possible other code in between)
ldr r4, =IO_ADDRESS
The equ directive allows us to give names to constants.
This helps make the code more readable.
It also helps with editing the code faster.
  To change the value of the constant, we just need to change the .equ line that assigns a name to the constant.
  Otherwise, we need to change the value of the constant in every single line that uses the constant.

## Slide 12: The ASCII and BYTE Directive
string_hello:
.ascii "hello world"
.byte 0x00
The above lines of code define a memory location that can be referred by the rest of the code as string_hello.
This memory location has the following contents:
  The ASCII codes for the characters in "hello world", followed by:
  A byte with content 0x00.

## Slide 13: Example of Usage
ldr r4, =IO_ADDRESS @ r0 := 0x 101f 1000
lrd r5, =string_hello
print_str:
ldrb r6,[r5]
cmp r6,#0x00 @ '\0' = 0x00: null character?
beq print_done @ if yes, quit
str r6,[r4] @ otherwise, write character
add r5,r5,#1 @ go to next character
b print_str @ repeat
print_done:

## Slide 14: The ASCIZ Directive
Strings typically have a '\0' character (ASCII code 0) at their end.
Instead of having to specify manually the null character at the end of the string, we can use the .asciz directive.
For example, instead of writing
string_hello:
.ascii "hello world"
.byte 0x00
We can just write:
string_hello:
.asciz "hello world"

## Slide 15: The WORD Directive
The byte directive specifies a byte of memory.
The word directive specifies a word of memory.
A word is 4 bytes in the ARM-7 architecture.
For example, consider this line of code in C:
int * array1 = {2014, 1914, 1814, 1714};
In assembly, you can write:
array1:
.word 2014
.word 1914
.word 1814
.word 1714

## Slide 16: Negative Numbers
In most modern architectures, negative numbers are represented using what is called "two's complement".
Suppose that your registers hold N bits.
The two's complement representation of number -X is: 2N - X.

## Slide 17: Negative Numbers: Examples
The two's complement representation of number -X is: 2N - X.
In ARM-7, N = 32.
How is number -1 represented:
  In binary?
  In hexadecimal?

## Slide 18: Negative Numbers: Example
The two's complement representation of number -X is: 2N - X.
In ARM-7, N = 32.
How is number -1 represented:
In binary:
  232-1 = 1 0000 0000 0000 0000 0000 0000 0000 0000 - 1
  = 1111 1111 1111 1111 1111 1111 1111 1111
In hexadecimal:
  232-1 = 1 0000 0000 - 1
  = 0x ffff ffff
If you call print_number with -1, you see 0xffffffff.

## Slide 19: Input
We have already seen how to print:
  What we have to do is store each ASCII code that we want to print into a specific memory address: 0x101f1000
To get text input from the user, we do something similar:
  We load an ASCII code from the same memory address: 0x101f1000
However, input is a little bit more complicated than output.
How does the program know that we have something to print?
  Easy: when the program hits an instruction that stores something to the designated address.
How does the program know that the user has entered text?
  Not so easy: the program hits an instruction that loads something from the designated address.
  However, is there something at that address? Has the user typed something yet?

## Slide 20: Input
To read a character of text, we will follow a simple approach (more sophisticated/efficient approaches are available):
  Wait until the user has entered a character.
  When the user has entered the character, read the character.
How can we know that the user has entered a character?
There is a specific memory address, that holds a specific bit, that:
  Is automatically set to 1 when the user enters some text.
  Is automatically set to 0 when we read that text.
This specific memory address is: 101f1018
The bit at position 4 in that address is set to 1 when the user has entered data.
  (Bit 0 is the least significant bit).

## Slide 21: Input
To read a character of text, we will follow a simple approach (more sophisticated/efficient approaches are available):
  Wait until the user has entered a character.
  When the user has entered the character, read the character.
How can we know that the user has entered a character?
There is a specific memory address, that holds a specific bit, that:
  Is automatically set to 1 when the user enters some text.
  Is automatically set to 0 when we read that text.
This specific memory address is: 101f1018
The bit at position 4 in that address is set to 1 when the user has entered data.
  (Bit 0 is the least significant bit).